## Slide 1
Axonic – Ultrasonic-Flowmeter
DN65-150
Date 00, 0000
ITRON Thermal Energy
©2016 ITRON CONFIDENTIAL PROPRIETARY
Notes: THIS COVER PAGE OFFERS THE OPTION TO ADD IMAGERY

## Slide 2: Axonic – What is Axonic?
Axonic is an ultrasonic static flow meter for heat and cooling applications
Axonic is the essential subassembly of a thermal energy meter.
Axonic serves our customers with outstanding metrological performance.
Axonic comes with unique features that allows Itron positioning in applications that are not accessible from other players.
What is Axonic ?

## Slide 3: Axonic – What is Axonic?
It‘s a static stand alone flow meter with Interface to calculators
needs to be combined with stand-alone calculator
  CF51, CF55, CF800 (or other brands)
  + Pair of T-sensors
Axonic is an ultrasonic static flow meter for heat and cooling applications
Heat Supply
Heat Return

## Slide 4: Axonic – What is Axonic?
It‘s a static stand alone flow meter with Interface to calculators
needs to be combined with stand-alone calculator
  CF51, CF55, CF800 (or other brands)
  + Pair of T-sensors
Axonic is an ultrasonic static flow meter for heat and cooling applications
Cooling Supply
Cooling Return

## Slide 5: Axonic – What is Axonic?
Axonic is an ultrasonic static flow meter for heat and cooling applications
Axonic is the essential subassembly of a thermal energy meter.
Axonic serves our customers with outstanding metrological performance.
Axonic comes with unique features that allows Itron positioning in applications that are not accessible from other players.
What is Axonic ?

## Slide 6: Axonic – What is Axonic?
The medium is challenging (magnetit, calcium….)
Networks operates 24h a day, 365 days a year (= permanent flow)
Ultrasonic is the best technology to survive (no wearing, no magnets)!
Axonic is the essential subassembly of a thermal energy meter.
Acoustic wave velocity: c+V
Acoustic wave velocity: c-V
FLOW
Velocity: V
Time of flight:
With the flow: t1 = d / (c+V)
Against flow: t2 = d / (c-V)
Q = K.t.(t)-²
d

## Slide 7: Axonic – What is Axonic?
Axonic is an ultrasonic static flow meter for heat and cooling applications
Axonic is the essential subassembly of a thermal energy meter.
Axonic serves our customers with outstanding metrological performance.
Axonic comes with unique features that allows Itron positioning in applications that are not accessible from other players.
What is Axonic ?

## Slide 8: Axonic – Metrologic Performance
Dynamic range up to R400H (standard calibration R250HV)
Example qp25m³/h (DN65) :
Axonic serves our customers with outstanding metrological performance.
Chart: 
| 0.01 | 0.1 | 1 | 10 | 100 | 1000
 | 100 | 150 | 200 | 250 | 300 | 350
Woltman R50
Ultrasonic R100
Axonic R400
Axonic R250
qi 1000 L/h
qs 30m³/h
qp 25m³/h qs 50m³/h
qi 250 L/h
qi 100 L/h
qi 63 L/h
qp 25m³/h / qs 50m³/h
qp 25m³/h / qs 50m³/h
Flow rate [m³/h]
R400 = Unique in the market
qi
qp
qs

## Slide 9: Axonic – Metrologic Performance
Axonic serves our customers with outstanding metrological performance.
qs
qp
qi
qc
qmax
Flow rate
Normal flow indication up to qmax
(pulse output equivalent to flow rate)
q > qmax (1,1x qs):
warning message
pulse output remains equivalent to 1,1qs
limited billing losses.
Axonic measures also when exceeding qmax

## Slide 10: Axonic – What is Axonic?
Axonic serves our customers with outstanding metrological performance.
Axonic measures also when exceeding qmax

## Slide 11: Axonic – Metrologic Performance
Accuracy class 2:
  Acceptance criteria: ± 2% (upper flow)
  Typical metrology expected to stay within ±1%!
Axonic serves our customers with outstanding metrological performance.
Chart: DN65 qp25
| 50 | 62.5 | 80 | 100 | 160 | 250 | 472.87080450158783 | 2500 | 12000 | 25000 | 50000
CEN+ | 5 | 5 | 5 | 5 | 5 | 4 | 3.0574 | 2.2 | 2.0417 | 2.02 | 2.01
CEN- | -5 | -5 | -5 | -5 | -5 | -4 | -3.0574 | -2.2 | -2.0417 | -2.02 | -2.01
100 | 0
250 | 0
ChW+ | 5 | 5 | 2 | 2 | 2 | 2 | 2
ChW- | -5 | -5 | -2 | -2 | -2 | -2 | -2
none
BC @ Hpos1 5c 51.5°C | -0.31886 | 0.31016 | -0.21957 | 0.06849 | 0.14329 | 0.11734 | 0.0018506 | 0.11238 | -0.028882 | -0.11046 | -0.11992 | -0.0060357 | -0.0066248 | -0.054225 | -0.20386
BD @ Hpos2 5c 51.5°C | -0.051252 | 0.88382 | 0.68841 | 0.41788 | 0.66434 | 0.46513 | 0.095106 | -0.21768 | 0.23088 | 0.14761 | 0.17628 | 0.15374 | 0.037525 | -0.071033 | -0.22834
none
BC @ Hpos1 3c 15.3°C | 1.8177 | 0.63269 | 1.207 | 0.57999 | 0.73203 | 0.10081 | 0.066716 | 0.062055 | 0.072623 | -0.22687 | -0.21172 | -0.16927 | -0.13176 | -0.0035259 | 0.065124
BD @ Hpos2 3c 15.3°C | 0.17868 | 0.60215 | 0.23542 | 0.434 | 0.23767 | 0.2522 | 0.066809 | -0.035754 | 0.1726 | 0.051476 | 0.056217 | 0.044492 | 0.025936 | 0.13356 | -0.064892
Accuracy channel
EN1434 class 2

## Slide 12: Axonic – Metrologic Performance
Fully concentric design
  flow sensivity class U0D0
  no need for straight length = smallest installation space!
All positions allowed - even diagonal and upside down!
Axonic serves our customers with outstanding metrological performance.

## Slide 13: Axonic – What is Axonic?
Axonic is an ultrasonic static flow meter for heat and cooling applications
Axonic is the essential subassembly of a thermal energy meter.
Axonic serves our customers with outstanding metrological performance.
Axonic comes with unique features that allows Itron positioning in applications that are not accessible from other players.
What is Axonic ?

## Slide 14: Axonic – Various Sizes
Various choice of lengths:
  standard length if standard length requested
  various special sizes for replacement market and new, if possible!
  example DN80 qp40
Axonic comes with unique features
L = 225mm
Replacement market
Mechanical Woltman
Market: Germany
+ All?
L = 200mm
Replacement market
Mechanical Woltman
Market: France
+All?
L = 300mm
replacement and new Woltman and Ultrasonic
Market: All
L = 350mm
replacement and new
Woltman and Ultrasonic
Market: France
+All?

## Slide 15: Axonic – Various Sizes
  Body type (DN, length, PN)
Axonic comes with unique features
Flanges PN16/25: EN 1092-2 97 tb 5+9 interface Type B (mobile and dismountable flanges)
Flanges PN40: EN 1092-1 97 tb 6+15 interface Type E (fixed flanges)
DN | QP | Length [mm] | PN [bar]
65 | 25 | 200 | 16
 |  | 300 | 16
 |  |  | 25
 |  |  | 40
80 | 40 | 200 | 16
 |  | 225 | 16
 |  | 300 | 16
 |  |  | 25
 |  | 350 | 16
 |  |  | 40
100 | 60 | 250 | 16
 |  | 360 | 16
 |  |  | 25
 |  | 400 | 16
 |  |  | 40
125 | 100 | 250 | 16
150 | 150 | 300 | 16
 |  |  | 40
 |  | 500 | 16
 |  |  | 25

## Slide 16: Axonic – Mobile Flanges
Mobile Flanges (PN16 & 25 versions):
  proven concept in C&I Water business (Flostar M)
  quick, safe and simple
  installation can easily be done by 1 plumber
Axonic comes with unique features

## Slide 17: Axonic – Insulation compliant
Insulation compliant
  Latest energy efficiency regulations require insulation of meters.
  Due to it’s “long-neck” design Axonic is compliant to full insulation (no overheating of PCB)
Axonic comes with unique features

## Slide 18: Axonic – Double pulse Output
Axonic provides a 2nd pulse output (B) (option)
Axonic comes with unique features
Output A: 4-wires:
Bat (+)
GND (-)
µCom communication
pulse-output (+)
Output A: Energy
(calculators  M-Bus / RF / GPRS  Emmsys / MDM)
Output B: 3-wires:
GND (-)
pulse-output (+)
direction flag
Note: pulse weight B can be different than pulse weight A!
Output B: Control system
(conncetion to any other device, e.g. for connection to heat control system or to monitor backflow).

## Slide 19: Axonic – UmCS Software
UMCS = Ultrasonic Meter Configuration Software
  reading – configuration - re-calibration - flow adjustement
  for RBUs, Distributers and Laboratories
Axonic comes with unique features
Passport
included

## Slide 20: Axonic – UmCS Software
Metrological Report Inside the meter!
  read-out with UMCS-Soft
  print-out with UMCS-Soft
Axonic comes with unique features

## Slide 21: Axonic – On Field tracking
2D Barcode contains serial number and meter details
  read-out with any barcode reader
Axonic comes with unique features
Meter Information coded in
2D Barcode

## Slide 22: Axonic – Intelligent Features
Axonic is intelligent
  information about status of the network and the meter itself
  status and alarms visible by LED
  communication of alarms to calculator
  vizualisation through AMR systems
    e.g. in Everblu, Emmsys
Status information that can be transmitted:
  flow detected
  air in Pipe
  US Asic Alarm
  low signal amplitude
  max flow alarm
  backflow alarm
  product in test mode
Axonic comes with unique features

## Slide 23: Axonic – What is Axonic?
Robust and reliable design:
  Medium temperature range: 1….130° (acc. 150°C)
  Ambient temperature range: -25°C… 60°C
  Environmental class
    EN1434: environmental class C
    MID: environmental class E2 (electromagnetic)
  environmental class M2 (mechanic)
  Body material:
    PN16/ PN25: bronce
    PN40: inox (stainless steel)
  IP68
Axonic comes with unique features

## Slide 24: Axonic – Summary & Highlights
2nd pulse output option
- Energy measurement
- Connect BMS system
Excellent Metrology
- High class 2 accuracy
- Oustanding dynamic range
- Insensitive to flow disturbances
- Reliable and repeatable
Ease of installation
- Mobile flange design
- No straight length required
- Installation in any position
- Various choice of length
Self-diagnostic intelligence
- Air in Pipe
- Backflow
- Dirty medium…
- Overflow
Internal memory
- Passport inside
- Test protocol inside
Robust and Reliable
- Medium 130°C permanent
- High Pressure versions (PN40)
Utility revenue protection
- Behaviour above qmax
- Low flow performance
Environmental friendly
- Thermal Insulation compliant
- External power supply

## Slide 25
qp 25 up to qp150
DN65 up to DN150
Accuracy EN1434 Class 2
Environmental class E2, M2 acc. EN1434
Temperature T: 1°C up to 130°C
PN16 / PN25 / PN40
power supply by the calculator (or battery or mains supply using the pulse box)
Data communication (e.g. dirty warning message) in case of use with CF51/55/800
2nd pulse output option
Internal memory
  Passport inside
  Test protocol inside
Summary
Axonic Summary